## Slide 1: DEVELOPMENT OF Smartphone integrated NANO SENSORs
Albert Chen
University of California, Riverside

## Slide 2: Introduction
US Department of Homeland Security
  Detection of Chemical Warfare Agents:
    Sarin Gas – Tokyo Subway (1995)
    Cyanide – WTC (1993)
  Detection of Explosive Devices
    Oklahoma City Bombing (1995)
    Airports to prevent Terrorist attacks
    Detection of Landmines
Industrial Detection of Toxic Chemicals
  Accidental Spills from Factory Incidents and Transportation Accidents

## Slide 3: CURRENT DETECTION METHODS
Detection Method | Advantages | Disadvantages
Detection Paper | Immediate Results Easy Operation | False Alarms Liquids Only
Gas Detection Tube | High Sensitivity | Slow Response One Time Use
Flame Photometric Detector | Quick Response and Recovery High Sensitivity | External Fuel Required
Ion Mobility Spectrometer | Rapid Detection Low Power Consumption | Expensive > $10k
Surface Acoustic Wavelength | Fully Automated | Low Sensitivity Large Device Slow Recovery

## Slide 4: Current development - nasa
NASA Ames Research Center
  Smartphone Integrated Device
Images adapted from NASA Ames Research Center

## Slide 5: OBJECTIVE
To develop a portable and wearable gas sensor device
  Low Cost
    ~$100 - ~$200 depending on components
  Fast response and recovery
  Multiple sensors
    Temperature
    Humidity
    GPS

## Slide 6: development
Software
Arduino Software Development
Android Software Development
Hardware
Increasing Signal-to-Noise Ratio
PCB Fabrication and Sensor Integration
Assembly
Smartphone Integrated Unit
Stand Alone Unit
Field Tests
Gathering Data/Building a Database
Development of Pattern Recognition Algorithms

## Slide 7: WHY ANDROID?
Most common smartphone OS and gaining market share
Open source development and lots of existing code
More flexible than iOS

## Slide 8: DEVICE COMPONENTS
Device | Data Transfer | Display | Power | Sensor
Smartphone Integrated Portable Device | Bluetooth | Smartphone | Battery | Gas
 |  |  |  | Biological
 | Wi-Fi |  |  | 
 |  |  | Solar Cell | Temperature
 | MicroSD | Tablet |  | Humidity
 |  |  |  | Pressure
 | USB |  | USB | 
 |  |  |  | GPS
Stand Alone Wearable Device | MicroSD | OLED | Battery | Gas
 |  |  |  | Biological
 |  |  | Solar Cell | Temperature
 | USB | Touch Screen |  | Humidity
 |  |  | USB | Pressure
 |  |  |  | GPS

## Slide 9: SMARTPHONE INTEGRATED DEVICE
Components
  Arduino Nano Microcontroller
  Humidity Sensor
  Temperature Sensor
  Bluetooth
  5V Battery
Data Management
  Real Time Graph
  Communicates with Smartphone or Tablet via Bluetooth
  Sensing results stored as .txt file on phone’s microSD card
    Can be sent via e-mail or copied off the microSD card

## Slide 10: SMARTPHONE APPLICATION

## Slide 11: STAND ALONE DEVICE
Components
  Arduino Nano Microcontroller
  Humidity Sensor
  Temperature Sensor
  GPS Module
  LCD Screen
  5V Battery
Data Management
  Results stored on microSD card

## Slide 12: Prototype of Portable device
Smartphone Integrated Nano-Chemiresistive Gas Sensor

## Slide 13: Prototype of wearable device
Wearable Sensor
Portable Device

## Slide 14: TESTING RESULTS
Bare SWNT sensing response against 20 ppm NO2 via Arduino
Chart: 
Bare SWNT sensing response against 20 ppm NO2 via Keithly
Time (s)

## Slide 15: FUTURE PLANS
Gas Sensor
  Wearable stand alone unit
  Portable stand alone unit
Biological Sensor
  Glucose Sensor
Software
  Developing and implementing pattern recognition patterns